## Slide 1: ECMP Based on Traffic Monitoring
Yi-Sung Chiu

## Slide 2: Outline
Introduction to ECMP
Inherent Problems
Architecture
Experiment
Demonstration

## Slide 3: Equal-Cost Multi-Path (ECMP)
Distribute flows to multiple paths
Load balancing
> Introduction to ECMP
- Inherent Problems
- Architecture
- Experiment Settings
Demonstration

## Slide 4: Simple Path Selection
Base on packet categories
  Split TCP and UDP packets by layer 4 protocols
Base on destination IP address
  Split packets sent to 140.113.1.0/24 and to 140.113.2.0/24 by subnets
> Introduction to ECMP
- Inherent Problems
- Architecture
- Experiment Settings
- Demonstration

## Slide 5: Next-Hop Selection (RFC2991)
Module-N Hash
  Module-N hash over packet header fields
Hash-Threshold
  Assign a unique range of hash output space to N next-hops
Highest Random Weight (HRW)
  A key for each next-hop by hash over header and address of next-hop
  Choose the largest key
> Introduction to ECMP
- Inherent Problems
- Architecture
- Experiment Settings
- Demonstration

## Slide 6: Inherent Problems
Collision is inevitable
  Especially with few paths but relatively more flows
Elephant flow occupies the link
  Other flows colliding with it will result in imbalance loading
- Introduction to ECMP
> Inherent Problems
- Architecture
- Experiment Settings
- Demonstration

## Slide 7: Next-Hop Selection on TM (I)
Monitor port statistics of packets/bytes transmission
Select next-hops by the least link usage
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration
Traffic Monitoring

## Slide 8: Next-Hop Selection on TM (II)
Flow 1
Flow 2
New Flow
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration

## Slide 9: Architecture
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration
Traffic Monitor
Controller
Flow Manager
Switches
PortStatsReply
PortStatsRequest
Packet-In
Packet-Out/FlowMod
PortStats

## Slide 10: Algorithm Flow Chart (I)
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration
Any multipath
Packet-In
Learning Bridge
YES
No

## Slide 11: Algorithm Flow Chart (II)
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration
Any Multipath for Dst
Multipath exist
No
Yes
Any MAC to port
No
Yes
Limit flooding
Flow-Mod/ Packet-Out

## Slide 12: Algorithm Flow Chart (III)
- Introduction to ECMP
- Inherent Problems
> Architecture
- Experiment Settings
- Demonstration
Is TCP/UDP
Dst exist multipath
Learn MAC to port
YES
No
Select group
Assign flow to least-load port

## Slide 13: Experiment Environment
Ryu controller
Mininet
2x2 leaf-spine topology
- Introduction to ECMP
- Inherent Problems
- Architecture
> Experiment
- Demonstration

## Slide 14: 2x2 Leaf-Spine Topology
of:0000000000000101
of:0000000000000102
of:0000000000000201
of:0000000000000202
1
2
1
2
1
1
2
2
3
4
3
4
Spine Switch
Leaf Switch
Host
- Introduction to ECMP
- Inherent Problems
- Architecture
> Experiment
- Demonstration

## Slide 15: Evaluation
Per-switch load balancing on ports
Use statistics from traffic monitoring
Achieve more accurate load balancing for links
  In extreme case of elephant flow existing, this method is much more efficient.
- Introduction to ECMP
- Inherent Problems
- Architecture
> Experiment
- Demonstration

## Slide 16
Demonstration
- Introduction to ECMP
- Inherent Problems
- Architecture
- Experiment Settings
> Demonstration

## Slide 17: Appendix (I) - Defect
Traffic engineering (TE) could give a more flexible method for load balancing and ECMP.
It is probably not such efficient and necessary in reality.

## Slide 18: Appendix (II) - Flow Match Rule
Flow Rule | Hard Timeout | Priority | Match Field | Actions
Learning Bridge | 0 | 3 | in_port, eth_dst, eth_src | Output
Select Group | 1000 | 1 | in_port, ethertype | Group
TCP/UDP Load Balancing | 1000 | 5 | ethertype, ipv4_dst, ip_proto, tcp_dst/udp_dst | Output

## Slide 19: Appendix (III) - Future Work
Consider more argument for next-hop selection
  Such as link QoS, cost, delay and so on
A formal configuration path, rather than hard-coded
  A further aim is to implement a topology manager, providing multipath information